Planning and Building Unit Tullamore, Co. Offaly. Telephone: 057 9324300 or 01 889 6400 Fax: 057 9324411 Web: www.education.ie

Room: Science Laboratory

Basic Science – LAB Equipment List and Specification

There are six lists for science equipment, i.e. LAB, RES, DAT, CHE, PHY and BIO. The provision of science equipment for science laboratories is as follows: One Basic Science List – LAB – for each science laboratory. One Science Resource List– RES – for each two science laboratories. iii) One Data List – DAT, Part 1 - for each two science laboratories. iv) One Biology List – BIO – for each Biology provision (in addition to i) and ii) above) plus Part 2 of DAT List. v) One Chemistry List – CHE –for each Chemistry provision (in addition to i) and ii) above) plus Part 3 of DAT List. vi) One Physics List – PHY – for each Physics provision (in addition to i) and ii) above) plus Part 4 of DAT List vii) Max. no. of Senior Lists: 3 for up to 4 labs; 4 for 5 labs; 5 for 6 labs. Note: Where the symbol ( is placed after a substance, a supplier who supplies a greater quantity than requested may be held responsible for removal and disposal of the excess.

Standards, Specifications and Conditions

All equipment shall be durable and safe for school use. Equipment wholly or partly funded from public funds is subject to inspection by officers from the Department of Education and Skills.

It is essential that tenders and tenderers for equipment for school use shall: Comply fully with the specifications and be durable and safe for school use. Comply fully with the standards as detailed and shall comply fully with European Standards (EN), both established and developing. Comply with European electrical standards and CE marking as appropriate. Fully comply with requirements in the Request for Tenders (RFT) document. Be accompanied by documentation of sufficient detail for full evaluation. Include the completed and signed certificate of compliance. Award of a contract is conditional on the production of a current tax clearance certificate. Failure to comply with the above may result in the tender being deemed null and void.

| Section 1: Basic Science Equipment |
| --- |
| Code Quantity | Descriptions and Specifications | Cost €: |
| LAB/100 24 | Bench mats, (asbestos free), round edges 3 mm thick, 150 x 150 mm |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/101 6 | Brushes, flask, curved bristle head, 50 m diameter x 100 mm long, with hinged centre joint, wood handle. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/102 6 | Brushes, test-tube, bristle fan shaped head, on wire handle, head diameter 10 mm. |  |
| LAB/103 1 | Draining rack, fitted with wall protecting back panel and fixing lugs to take 30 test-tubes and 12 flasks or beakers |  |
| LAB/104 5 | Filter paper, general purpose, grade 1, diameter 12.5 cm, box 100 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/105 5 | Filter paper, general purpose, grade 1, diameter 11 cm, box 100 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/106 1 | Absorbent paper (blotting paper), pack of 10 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/107 1 | Reel dispenser for laboratory paper, galvanised, Milaroll or equivalent. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/108 2 | Paper roll, Milaroll or equivalent, green, 300 mm wide, to suit above |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/109 1 | Rubber stoppers, solid, assorted sizes x 100 per pack. To BS 2775 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/110 1 | Rubber stoppers – ‘One Holed’. assorted sizes (100 per pack). |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/111 1 | Rubber stoppers – ‘Two Holed’. assorted sizes (100 per pack). |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/112 5 | Test paper reels, pack of 4 dispenser reels; each reel contains a paper strip 5 m long x 6 mm wide, supply as: 2 reels x pH 1-14 1 reel as Litmus blue 1 reel as Litmus red |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/113 5 | Tubing connectors, polypropylene, packs of 10, straight, for tubing bore 7-9 mm |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/114 5 | Tubing connectors, polypropylene, packs of 10, T-shape, for tubing bore 7-9 mm |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/115 5 | Tubing connectors, polypropylene, packs of 10, Y shape, for tubing bore 7-9 mm |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/116 2 | Tubing cutter, for normal wall plastic and rubber tubing, up to 19 mm o.d., with spring loaded hardened steel blade. |  |
|  | Manufacturer: | Catalogue No: |  |

| LAB/117 6 | Spare blade for above |  |
| --- | --- | --- |
|  | Manufacturer: | Catalogue No: |  |
| LAB/118 12 | Tiles, polypropylene, white, 12 cavities |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/119 12 | Tiles, plain, ceramic, flat, white, 100 x 100 mm |  |
| LAB/120 12 | Bench lamp, angle-poise, switch on shade, base weighted for stability, max 60 W bulb, stand finished in enamel, inside of shade finished in white gloss, maximum working height 750 mm, complete with 2 m, 2-core mains cable. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/121 1 | Beehive shelf, diameter 75 mm |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/122 1 | Chopping board, hardwood, kitchen type |  |
|  | Manufacturer: | Catalogue No: |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/123 12 | Hoffman clip, internal opening 30 mm. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/124 1 | Knife, glass cutting with replaceable blades |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/125 1 | Scissors, general purpose, stainless steel, moulded plastic handles, 200 mm long |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/126 1 | Scissors, heavy duty, scalloped blades, mix of left and right hand grips |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/127 12 | Mortar and Pestle, unglazed inside, external diameter 140 mm. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/128 12 | Mohr clip, overall length 50 mm. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/129 24 | Spatula, polypropylene, flat, tapered with chamfered ends, length 100 mm |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/130 12 | Wash bottles, Polythene, oval, capacity 250 cm3 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/131 | Moved to RES List |  |
| LAB/132 2 | Lids, gabled, stainless steel, to suit above |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/133 10 | Stainless steel racks to suit above, 16 x 26 mm holes |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/134 2 | Test tube racks, polypropylene, weighted, 40 holes diameter 25 mm, to suit above |  |
|  | Manufacturer: | Catalogue No: |  |

| LAB/135 12 | Bunsen burner, heavy diecast base, integral inlet tube for 8 mm bore flexible gas tubing, base finished in chemical resistant acrylic paint. Suitable for use with LPG or natural gas, as required by the school. Overall height 124 mm, o.d. of burner tube 13 mm, with rotatable air regulator. |  |
| --- | --- | --- |
|  | Manufacturer: | Catalogue No: |  |
| LAB/136 12 | Tubing, bunsen burners, neoprene rubber, reinforced ends, length 600 mm |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/137 2 | Gas lighter, piezo-electric |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/138 1 | Kettle, c. 1.7 L, cordless, automatic cut off, removable lid, spout fill facility, water level indicator, 230 V |  |
|  | Two year warranty. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/139 12 | Crucible tongs, straight, length 150 mm. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/140 12 | Crucible tongs, bow, length 150 mm |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/141 12 | Tongs, bowed, for beakers 100 cm3 – 500 cm3 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/142 3 | Combustion spoons, steel with flange cap (diam. 90mm), overall length 400 mm. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/143 12 | Crucibles, porcelain, low form, nominal capacity 25 cm3 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/144 12 | Crucible lids for above |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/145 3 | Heat sensitive paper to indicate thermal conductivity and radiation, pack |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/146 12 | Iron wire gauzes, ceramic centres, 125 x 125 mm. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/147 6 | Bimetallic strip fitted with handle |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/148 6 | Ingenhausz apparatus, metal tank with legs, 210 x 75 x 75 mm with 7 inlets to take six rods of copper, iron, lead, brass, zinc and aluminium mounted in corks with remaining hole for thermometer |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/149 6 | Thermal conductivity rods (aluminium, brass, copper, glass and iron), 250 x 3 mm, length x diameter, set of 5, for LAB/148 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/150 12 | Pipeclay triangles, on iron wire, side length 65 mm. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/151 12 | Thermometer, range – 10 to 110 (C by 1 (C divisions, spirit filled (red), 305 mm length |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/152 12 | Thermometer, fever strip, graduated 36.5 to 40.5 (C x 0.2 (C. |  |
|  | Manufacturer: | Catalogue No: |  |

| LAB/153 2 | Thermometer, clinical, digital, range 32 to 42 (C with LCD temperature indication to 0.1 (C, powered by 1.5 V silver oxide battery, supplied complete with battery |  |
| --- | --- | --- |
|  | Manufacturer: | Catalogue No: |  |
| LAB/154 6 | Thermal conductivity of metals set, 4 different metal strips (aluminium, brass, copper and iron) on wooden ring, cavity for wax on end of strip |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/155 6 | Convection tube, glass, internal diameter 20 mm, rectangular structure with funnel on top |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/156 6 | Ventilation apparatus, metal box, 22 x 10 x 10cm with removable glass front and two chimneys on top |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/157 30 | Retort clamp, rubber covered jaws, clamping tommy-bar screw-through swivels, mounted on 135 mm cast alloy rod. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/158 12 | Retort stand rings with boss heads suitable for fastening on rods of diameter 8 – 13 mm. External diameter 75 mm. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/159 30 | Retort stand rods, aluminium, screwed M. 10, diameter 10 mm, length 400 mm. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/160 30 | Retort stand base, steel, 250 x 160 mm, rubber feet, tapped hole (10 x 1.5 mm metric thread) at one end for retort rod, corrosion resisting paint finish. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/161 30 | Bossheads, cast alloy, two slots at right angles, for rods up to 16 mm diameter, 120 x 30 mm, length x diameter. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/162 12 | Clamps to hold object up to 90 mm diameter, corrosion resistant. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/163 6 | Stands, double funnel. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/164 12 | Stands, boiling tube, hard wood with polypropylene end supports, supplied as kit for assembly by user, 6 holes x 32 mm diameter. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/165 12 | Tripod stands triangular top, length of side arm 150 mm, height 200 mm, cast iron. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/166 24 | Test-tube holders, hardwood, with steel spring |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/167 12 | Test-tube rack, polypropylene, 25 mm hole diameter, 6 holes, 6 pegs, supplied as kit for assembly by user. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/168 12 | Expansion of liquid apparatus, 5 bulb tubes, 40 mm diameter with stems 300 mm long in frame, with scales, housed in metal trough |  |
|  |  | Catalogue No: |  |
| LAB/169 1 | Displacement vessel, large, with spout, 180 x 110 mm. |  |
|  | Manufacturer: | Catalogue No: |  |

| LAB/170 12 | Displacement vessel with spout, approximately 100 x 65 mm. |  |
| --- | --- | --- |
|  | Manufacturer: | Catalogue No: |  |
| LAB/171 12 | Electrostatics kit, elementary experiments in electrostatics, comprising polystyrene spheres, cotton cloth, woollen cloth, wooden clothes pegs, nylon filament, small paint brush, graphite in alcohol, insulators, pins, acetate and vinyl strip, instructions for use |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/172 1 | Electroscope, metal aluminium vane, 50 mm diameter charging disc mounted on metal casing with removable glass side panels |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/173 12 | Magnets, bar, triconal type, 50 mm length, complete with keepers. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/174 3 | Compass, plotting, 16 mm diameter, pack 10 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/175 12 | Buzzer, miniature transistor oscillator, 6 volt supply, mounted with 4 mm sockets |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/176 12 | Bezel push fit panel clip for 5 mm LEDs, mounting hole 8 mm, prominent position styles, pack 5 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/177 3 | Bulb holder, MES, socket E 10, pack 10. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/178 3 | Fuses, quick blow, 500 mA, pack 10 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/179 3 | Flashlamp bulbs, MES cap, round, 2.5 V, 300 mA, socket E 10, pack 10. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/180 3 | Fuses, quick blow, 1 A, pack 10 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/181 3 | Fuses, quick blow, 2 A, pack 10 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/182 3 | Fuses, quick blow, 5 A, pack 10 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/183 1 | Fuse wire, tinned copper, 2 A, reel 100 g |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/184 1 | Fuse wire, tinned copper, 5 A, reel 100 g |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/185 12 | LT variable voltage power supply unit, overload protection, Performance (approx): No Load 8 A Load d.c. 0-25 V 24 V a.c. 0-25 V 24 V |  |
|  | Two year warranty. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/186 3 | Light emitting diodes, standard, 5 mm, suitable for PCB or panel mounting, red, pack 5 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/187 3 | Light emitting diodes, standard, 5 mm, suitable for PCB or panel mounting, green, pack 5 |  |
|  | Manufacturer: | Catalogue No: |  |

| Section 2: Basic Science Equipment |
| --- |
| LAB/200 3 | Light emitting diodes, standard, 5 mm, suitable for PCB or panel mounting, yellow, pack 5 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/201 3 | Light emitting diodes, standard, 5 mm, suitable for PCB or panel mounting, with in-built IC to produce a continuous flashing, 9-12 V d.c., pack 5 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/202 12 | Light emitting diode holder (soldering not required) complete with 200 mm leads and LED release tool |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/203 12 | Newton's disc, 180 mm diameter (approx.), mounted on a metal stand and driven with a hand wheel |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/204 12 | Light pen |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/205 24 | Multimeters, digital, autoranging frequency measurement, capacitance measurement and transistor test. Voltage a.c.& d.c. – 5 ranges each from 200 mV x 100 µV to 600 V x 1 V. Current a.c. & d.c. – 4 ranges each from 2 mA x 1 µA to 10 x 10 mA. Resistance 6 ranges from 200 R x 0.01 R to 20 M x 10 k. Capacitance – 5 ranges from 2000 pF x 1 pF to 20 µF x 10 nF. Frequency – 5 ranges 2 kHz x 1 Hz to 20 MHz x 100 kHz. Diode Test. Continuity test. Transistor test NPN and PNP. |  |
|  | Two year warranty. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/206 12 | Resistor, light dependent, cadmium sulphide cell LDR in glass case with clear end window |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/207 2 | Resistor, carbon film resistors 0.5 W with maximum working voltage of 350 volts, 47 R, pack of 10. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/208 2 | Resistor, carbon film resistors 0.5 W with maximum working voltage of 350 volts, 100 R, pack of 10. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/209 2 | Resistor, carbon film resistors 0.5 W with maximum working voltage of 350 volts, 200 R, pack of 10. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/210 1 | Resistor, carbon film resistors 0.5 W with maximum working voltage of 350 volts, 1K, pack of 10. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/211 2 | Switches, push type, to make, non-locking, rated 250 mA, 125 V a.c., pack 10 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/212 1 | Push switches, to break, non locking, rated 250 mA, 125 V AC, pack 10 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/213 12 | Keys: contact type one-way |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/214 6 | Transistor, general purpose, BC108 NPN power, pack 5. |  |
|  | Manufacturer: | Catalogue No: |  |

| LAB/215 6 | Transistor, general purpose, ZTX 300 NPN audio, pack 5. |  |
| --- | --- | --- |
|  | Manufacturer: | Catalogue No: |  |
| LAB/216 6 | Transistor, general purpose, BFY51 NPN audio, pack 5. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/217 6 | Connecting leads set, flexible PVC lead, plug and socket 4mm diameter, nickel-plated, fully insulated, comprising 2 x red 100 cm 2 x blue 100 cm 2 x red 50 cm 2 x blue 50 cm 2 x red 25 cm 2 x blue 25 cm 4 x black 100 cm 6 x black 50 cm 6 x black 25 cm 4 x black 10 cm |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/218 150 | Crocodile clips with shank to accept 4 mm plugs, length 40 mm. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/219 12 | Metre rules, horizontal reading, cm and mm |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/220 12 | Opisometer. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/221 3 | Balance, electronic, top-loading, capacity 1200 g, capable of weighing to a precision of both 0.1g and 0.01 g, LCD display, zero tare, stainless steel weighing pan, a.c. mains supply, 230 V. |  |
|  | Two year warranty. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/222 12 | Balances, Spring, Flat form, zero adjuster, overload protection, hook, in metal case, reading in Newton (N), 10 N x 0.2 N |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/223 12 | Magnifiers, light weight, pocket size, two plano-convex lenses, lens mount folds into case, 1.5 cm (diameter) x 2 cm (depth), magnification x10. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/224 2 | Mirror, plane, glass 100 x 75mm, pack 10 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/225 2 | Holder for plane mirror, above, hardwood cube with slot, per pack 10, for above |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/226 3 | Magnifier, hand held, acrylic lens, frame and handle, magnification x 3.4, lens diameter 48 mm. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/227 2 | Pins, optical, pack 100 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/228 24 | Springs, steel, extension, 6mm diameter, closely wound, length 150, extension for 250 g load approx. 250mm |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/229 12 | Scale pan, with cords and hooks |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/230 1 | Bell in bell jar apparatus, 3 V a.c./d.c. supply |  |
|  | Manufacturer: | Catalogue No: |  |

| LAB/231 1 | Generator, low frequency, converts d.c. into a.c. at frequencies up to 30 Hz |  |
| --- | --- | --- |
|  | Manufacturer: | Catalogue No: |  |
| LAB/232 1 | Air pump, pressure or vacuum, two riffled connections one each for vacuum and pressure, hand operated |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/233 12 | Filter pumps, vacuum, water-jet, without pressure gauge, Polypropylene, with tapered side arm, maximum vacuum approx. 25 mm Hg at a flow rate of approx. 17 litre/minute. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/234 6 | Microscope, monocular, 10x eyepiece, low voltage illumination 12 V/20 W built-in, 140 x 140 mm mechanical stage, 3 objectives 4x/0.1, 10x/0.25, 40x/0.65, triple nosepiece, lenses coated, separate coarse and fine focusing, built-in safety lock to protect slides. The 40x objective spring-loaded, condenser with iris diaphragm and centring ring, rack and pinion focusing, a.c., 230 V, 50 Hz supply. Supplied with spare bulbs, fuses, plan/concave orientable mirror, dust cover. Inclines, rotatable viewing tube or conventional inclinable body, stage with side clips |  |
|  | Two year warranty. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/235 2 | Microscope slides, 75 mm x 25 mm, box 100. Suitable for routine and student use |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/236 2 | Cover slips, box 100, square. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/237 1 | View Cam, Flat base, flexible arm, Lens x10, mains a.c., 230 V, 50 Hz |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/238 4 | Microbiological inoculating wire, 50 mm, pack of 20 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/239 12 | Microbiological inoculating loop handles for inoculating wire, aluminium & nickel plated, brass collar, length 150 mm |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/240 12 | Respiration apparatus, for tests on inhaled and exhaled air, comprising two test-tubes (150 x 19 mm) each with two-holed stoppers and two lengths of 5 mm glass tubing. One short and one long tubing piece is connected via PVC tubing to a mouth T-piece |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/241 12 | Respirometer, simple type to compare rates of absorption or evolution of gases by small organisms during respiration. Complete with instructions and wire baskets to support the organisms |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/242 6 | Scalpel blades, no 22, surgical quality, to fit handles above, packs 5 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/243 6 | Scalpel handles, polystyrene, disposable, length 135 mm approximate length, packs 10 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/244 12 | Forceps, stainless steel, blunt end, without guide pin, 115 mm long |  |
|  | Manufacturer: | Catalogue No: |  |

| LAB/245 1 | pH Meter, digital, suitable for routine laboratory operations, choice of pH, mV or (C readout, electrode stand and mains adaptor, a.c. 230 V supply, complete with 2 m cable. |  |
| --- | --- | --- |
|  | Two year warranty. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/246 12 | Voltameter, Hoffmann, hand-held for student use, comprising of embedded platinum electrodes connected to 4 mm terminal connections, two test tubes, overall construction of acid-proof plastic. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/247 12 | Timer/clock/stopwatch, min. 10 mm LCD display, reading to 0.01 second, with memory, 24 hour capacity, with batteries. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/248 1 | Chart: size approximately 100 x 75 mm or nearest equivalent, coloured to illustrate the following: Biology: Fruit and seed dispersal Pollination and fertilisation Flowers and inflorescences Fruit dissemination and germination Circulatory system in the body Male and female reproductive system Plant structure Human digestive system Chemistry: How the bunsen burner works. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/249 1 | Chart, wall mounted, Periodic Table of the Elements, laminated, 140 x 100 cm |  |
|  | Manufacturer: | Catalogue No: |  |

| Section 3: Glass and Polypropylene ware |
| --- |
| LAB/300 3 | Gas jars, heavy glass, ground flange, 150 mm high x 50 mm internal diameter |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/301 1 | Gas jar covers, circular sheet glass, for 50 mm int. diameter jars, pack 10 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/302 12 | Bottles, indicator, dispensing, clear glass, plastic stoppers, vinyl teat and graduated pipette, 60 cm3 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/303 3 | Trough, pneumatic, heavy glass, cylindrical, 250 ( 125 mm (diam x height) |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/304 3 | Glass rods, soda lime, diameter 8 mm, in lengths 1.5 m, bundle 5 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/305 24 | Beaker, borosilicate glass, 100 cm3, graduated, with spout |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/306 24 | Beaker, borosilicate glass, 250 cm3, low form, graduated, with spout |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/307 12 | Beaker, borosilicate glass, 400 cm3, low form, graduated, with spout |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/308 12 | Measuring cylinder, borosilicate glass with glass foot, graduated, 100 cm3 x 1 cm3 graduations, with spout |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/309 12 | Measuring cylinder, borosilicate glass with glass foot, graduated, 250 cm3 x 2 cm3 graduations, with spout. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/310 12 | Dropping bottle, clear glass with polythene stoppers fitted with glass dropper and vinyl teat, nominal capacity 125 cm3 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/311 12 | Flask, conical, borosilicate, wide mouth, graduated, 100 cm3 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/312 24 | Flask, conical, borosilicate, wide mouth, graduated, 250 cm3 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/313 12 | Flask, round bottom, borosilicate, 250 cm3 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/314 24 | Funnel, conical, plain soda glass, 150 mm diameter. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/315 2 | Test-tubes, glass, borosilicate, medium wall, with rim, size 125 mm x 16 mm, pack 100 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/316 1 | Boiling tubes, glass, borosilicate, medium wall, size150 mm x 24 mm, pack 100 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/317 1 | Pipettes, disposable, graduated with integral bulb, translucent, length 155 mm, inert polythene, 3 x 0.5 cm3 (capacity x graduation), pack of 500. |  |
|  | Manufacturer: | Catalogue No: |  |

| LAB/318 12 | Stirring rod, glass, one end round, other flat, length 200 mm |  |
| --- | --- | --- |
|  | Manufacturer: | Catalogue No: |  |
| LAB/319 12 | Watch glasses, borosilicate, clear glass with ground edges, 100 mm diameter. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/320 6 | Dispenser, bottle top, suitable for aqueous solutions, dilute acids and strong alkaline solutions. Volume can be set and locked, 45 mm thread with 32 and 40 mm adapters. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/321 24 | Evaporating basin, porcelain, semi-deep with spout, Capacity, 75 cm3; 82 ( 32 mm |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/322 10 | Reagent bottles, amber glass, narrow mouth with interchangeable dustproof polythene stoppers with hexagonal heads, capacity 250 cm3 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/323 10 | Reagent bottles, clear glass, narrow mouth with interchangeable dustproof polythene stoppers with hexagonal heads, capacity 250 cm3 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/324 6 each | Reagent bottles, labelled, clear or amber (A) glass, narrow mouth with interchangeable dustproof polythene stoppers with hexagonal heads or glass stopper, as appropriate, capacity 250 cm3 Ethanoic (acetic acid), dilute Ammonia solution, dilute Copper(II) sulfate Fehlings solution 1 Fehlings solution 2 Hydrochloric acid, dilute Lime water Potassium iodide Sodium hydroxide, dilute |  |
|  | Manufacturer: | Catalogue No: |  |

| Section 4: Safety Equipment |
| --- |
| LAB/400 24 | Laboratory coats, white, cotton, front snap fasteners, range of sizes 36-44, length approx. 105 cm, one breast and two side pockets |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/401 30 | Safety glasses, with side protection, should be capable of use over spectacles, adjustable sizes type. To Standard EN 166. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/402 2 | Eye-Wash Bottle, contoured eye-cup, capacity 500 cm3 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/403 1 | Fire Blanket, glass fibre, 80 cm ( 92 cm |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/404 1 | Eye wash station complete with two x 500 cm3 saline eye wash containers. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/405 2 | Disposable eye baths, box 12. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/406 1 | First aid cabinet, c. 450 x 330 x 200 mm, metal, lockable, for wall mounting, complete with shelving, including shelving on inside of doors, to include plaster strip, rowa rolan, burn shield, burn gauze, cotton bandages, triangular bandages, zinc oxide tape, cotton wool, cotton buds, tube gauze, CPR mouth piece, gauze swabs, antihistamine cream, ‘savlon’ cream, burn cream, eye pads, optrex, dettol, scissors, forceps, safety pins, gloves, wound wipes, one shot eye wash, absorbent lint, ice pack, wound dressings, burn dressings, crepe bandage, ambulance pads, plasters. |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/407 6 | Gloves, heat resistant – 230° for 15 s , 1 pair per pack, medium |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/408 2 | Gloves, disposable, latex, large, pack 100 |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/409 3 | Gloves, heavy duty, red PVC, medium, 7.5, length 270 mm; pack a pair |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/410 1 | Safety screen, polycarbonate panels (3) hinged, 610 mm high, outer panels, 230 mm wide, centre panel 300 mm wide, polypropylene bases for clamping/screwing to bench |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/411 3 | Clamp, metal, 50 mm opening for use with safety screen above |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/412 1 | Spill disposal kit, 5 L capacity container kit, with absorbent mats, 1 kg particulate absorbent, plastic disposal bags, wrap ties, scoop, brush, chemical resistant gloves and chemical goggles |  |
|  | Manufacturer: | Catalogue No: |  |
| LAB/413 1 | Fire bucket |  |
|  | Manufacturer: | Catalogue No: |  |

| Equipment for Science (Laboratory) Four Sections |
| --- |
| Section | Code Quantity. | Descriptions & Specifications: | Total Cost €: |
| Section 1 | LAB/100–LAB/187 | Basic Science Equipment. |  |
| Section 2 | LAB/200–LAB/249 | Basic Science Equipment |  |
| Section 3 | LAB/300–LAB/324 | Glass and Polypropylene Ware |  |
| Section 4 | LAB/400–LAB/413 | Safety Equipment |  |
| Sub-total: € |  |
| Add for VAT: € |  |
| Total Amount for LAB List: € |  |

Standards, Specifications and Conditions

All equipment shall be durable and safe for school use. Equipment wholly or partly funded from public funds is subject to inspection by officers from the Department of Education and Skills.

It is essential that tenders and tenderers for equipment for school use shall: Comply fully with the specifications and be durable and safe for school use. Comply fully with the standards as detailed and shall comply fully with European Standards (EN), both established and developing. Comply with European electrical standards and CE marking as appropriate. Fully comply with requirements in the Request for Tenders (RFT) document. Be accompanied by documentation of sufficient detail for full evaluation. Include the completed and signed certificate of compliance. Award of a contract is conditional on the production of a current tax clearance certificate. Failure to comply with the above may result in the tender being deemed null and void.

| Certificate of Compliance with Standards, Specifications and Conditions |
| --- |
| I/We certify that the equipment tendered complies in all respects with the Standards, Specifications and other requirements/conditions specified in this tender document and in the Request for Tenders (RFT). I/We hold a current tax clearance certificate. |
| Company: |  |
| Signed: |  | Date: |  |
| Position: |  |  |  |