Survey Report OF NOISE RISK ASSESSMENT

| School / Dept / Unit | CEDAR, School of agriculture |
| --- | --- |
| A: Identifying workplace hazards and existing controls |
| 1. Brief summary of work activity or project assessed | All activities where staff or visitors are involved in Feed mill Dairy Unit Applied Unit APRU Operating vehicles |
| 2. List significant hazards | Noise |
| 3. Relevant University or local guidelines or standards | AS8 leaflet on noise – Farms Safety Manual FASTCo/HSE leaflet Noise and hearing conservation – Farms safety Manual Farmwise booklet – Farms Safety Manual Chainsaw safe working procedure |  |
| 4. List who might be exposed to the hazards (e.g. staff, students, visitors, consider numbers at risk) | Staff Student Visitors and Contractors |
| 5. How might they be harmed? (type of injury or health problem that might result) | Noise induced hearing lost from long term noise exposure Temporary noise affects such as tinnitus Develop Stress related symptoms as noise is a stressor Inability to hear other warnings Lack of concentration |
| 6. List control measures in place to reduce risks Assess whether these controls are adequate, actually used in practice and regularly checked, where appropriate. | Ear protection zones in Applied Unit, Mill Warning signs on feed mixer Metabolism Unit PPE ie ear defenders worn in some areas Tractors with Q cab used designed to prevent noise exposure above 85dB(A) Limited work times in vicinity of high noise exposure Job rotation and multi-tasking ensures that staff and students are not subjected to noise continuously Occupational Health questionnaire includes noise and identify staff working in high noise areas |
| B: Assessing the level of risk and further action needed |
| 7.1 How severe is any injury or health effect likely to be? | Tick one box (S =score given in brackets) | Minor  (1) | Serious ☑ (2) | Major  (3) | Fatal  (4) |
| 7.2. How likely is exposure to the hazard? | Tick one box (P =score given in brackets) | Very unlikely  (1) | Unlikely  (2) | Possible  (3) | Likely ☑ (4) |
| 7.3. Calculate the risk score by multiplying the 2 scores in Q7.1 & 7.2 | Risk Score (s x P) = | Low  (13) | Medium (46) | High ☑ (89) | Very High  (1216) |

| 8. Immediate further action to be taken to make the situation safe / reduce risk to health | Action to be taken by whom? | Implementation Date |
| --- | --- | --- |
| 9. Further action or additional controls needed to reduce risk as low as reasonably practicable | Action to be taken by whom? | Implementation Date |
| 1. Specification for work plant and equipment to achieve lowest noise and vibration emission 2. Vehicle and plant maintenance regime to be implemented so that eg loose panels and unbalanced rotating parts are attended to. Ensure that engineering means of reducing noise, eg anti vibration mounts, silencers, dampeners are implemented whenever possible. 3. Reporting scheme for defects in Tractor and Q cabs to be instigated. 4. Staff reminded on the need to ensure windows and doors closed to ensure low noise levels are maintained 5. Where there are defects on cabs, as a temporary measure either reduce amount of work or if not possible provide and ensure operators wear ear protection 6. Tractors without cabs are likely to have noise levels above 90dB(A) and drivers must wear ear protection 7.All areas where noise levels are 85dB (A) and above to have warning signs and staff recommended to wear ear defenders to BS EN 352 regardless of length of time. 8. Areas 90 dB(A) mandatory hearing protection areas to be provided warning signs and ear protection worn. 9. Staff reminded to limit work in noisy areas or with noisy machinery whenever possible 10. Additional ear defenders to be provided for visitors and Supervisor/Area manager to ensure they are worn. 11. Staff reminded on the need to wear Ear defenders correctly, to maintain and clean and to report loss, defect to their line manager. 12. Staff provided with Protect your hearing leaflet from HSE INDG299 13. Contractors to be warned of high noise areas of the Farm. 14. See attached report for specific recommendations. 15. Staff in high noise areas, working on machinery and plant and dairy operations to undergo health surveillance from Occupational Health |  |  |

| Name of Assessor (please print) | Debbie Sullivan |  |  |
| --- | --- | --- | --- |
| Signature of Assessor |  | Date: September 04 |  |
| Signature of Head of Dept/School/Unit |  | Date: |  |
| Date for Review (maximum 12 months from date of assessment) | May 2005 |

Noise survey of typical high noise operations

| Measurement Details |  |
| --- | --- |
| CEL Model: 573 Type C2 Windshield used |  |
| Serial number: | 3/0421998 |
| Owner: | Health and Safety Services |
| Calibrated: | CEL 282, serial 3/06225358 |

| Area/Plant | Noise Level dB(A) | Observations/Notes | Recommendations |
| --- | --- | --- | --- |
| Feedmill |
| Augers | 70 | 2 hour typical operation in morning and 1 hour afternoon | Recommendation staff is not in vicinity when mixing but if necessary ear defenders worn. Warning sign erected |
| Mixer empty | 74 |  |  |
| Mixer full | 84 (86 in very close proximity) |  |  |
| Feedstuff exiting auger | 86 |  |  |
| Metabolism Unit |
| Slurry scraper | 79 | 2x 20 min operations per day | Operator of mixer to comply with warning signs and wear ear defenders. Staff not to work in vicinity of both scraper and mixer |
| Mixer | 83 Rear 86.2 Front | 2 hours maximum PPE signs noted, but not worn |  |
| Dairy cleaner | 79 | 1 hour per day, staff not necessarily always present |  |
| Mixer and Scraper together | 88 front near mixer 85.6 near scraper |  |  |
| Applied Unit |
| Mill grinding room | 92 | Taken within room Signage available Ear defenders worn, max time 1 hour | Maintenance aspects to be checked. Mandatory hearing protection zone and wearing of ear defenders enforced. |
| Feed trucks | 78 | 2 hours |  |
| RMH | 87 | 4 hours but staff within proximity for minutes | Minimise time staff in vicinity |
| Hispec 2650 tractor | 86 | 2 hours | Warning sign and ear defenders should be provided |
| Area | Noise Level | Observations | Recommendations |
| Blue Feeder Wagon | 76 | Inside cab |  |
| John Deere 2650 | 73.5 | Check on Q-cab, taken at normal operating. |  |
| APRU |
| Pony | 88 | 1 hour operation, ear defenders worn | Warning signs and recommendation of wearing ear defenders |

Explanation of decibel dB values

The noise at work regulations have 2 main action levels related to daily personal noise exposure, 85dB(A) the first action level and 90 dB(A) the second action level,. Decibel is the measure unit for noise exposure and the (A) relates to a scale used which closely relates to the human ear response. These measurements are based on an 8 hour day

Very roughly speaking you can check whether levels are around 85dB (A)if you can hear clearly what someone is saying 2 metres away.  If you cannot hear them clearly when they are 1 meter away levels are likely to be around 90dB(A).

Every 3 dB (A) above the first action level halves the safe time that can be worked at that level eg someone working at  88dB (A) could only work safely for 4 hours per day.

Remember that the effects are cumulative.

Although it is mandatory to mark ear protection zones when 90 dB(A) is reached and ensure staff and visitors are wearing ear protection, it is good practice to ensure staff take precautions in all noisy areas and therefore it should be general practice to wear ear defenders in areas of 85 dB(A) or above.

NOTE:

Next year 2005, new regulations are likely to be introduced that will reduce the action levels to 80 and 85 respectively.

# Text boxes

Ref. No.